## Slide 1: Faster hologram generation by using Max- Depth-Range-Length method
MD SIFATUL ISLAM
Masters student, OIP lab, Chungbuk National University
Email : sifatul@CBNU.ac.kr

## Slide 2: Table of contents
Motivation
Conventional Multiple Wavefront Recoding Plane (M-WRP) method
Proposed Max-Length-Depth-Range (MLDR) method
Results and Summary
Future work

## Slide 3: Motivation
Point cloud of real objects => depth ranges => discreet distance between WRP and object points
  Long computational time
  Non- uniformity in color

## Slide 4: Conventional Multiple Wavefront recording plane (M-WRP) method
M-WRP calculates CGH in following steps:
Depth range is created with fixed number of depth layers
WRP in the center of each depth range
The light wave from 3D objects is recorded respective WRP [Equation. 1]
Light wave from WRPs to CGH is diffracted calculation based on fast Fourier transform (FFT)
Equation. 1
Equation. 2
Depth range 1
Depth range 2
Depth range 3
Depth range k
Diffraction
CGH
θ
WRP 2
WRP k
WRP 3
WRP 1
Notes: 1. Tomoyoshi Shimobaba, Nobuyuki Masuda, and Tomoyoshi Ito, "Simple and fast calculation algorithm for computer-generated hologram with wavefront recording plane," Opt. Lett. 34, 3133-3135 (2009)

## Slide 5: Max-Depth-Range-Length (MDRL) method
Depth range 1
Depth range 2
Depth range 3
Depth range k-1
Diffraction
CGH
θ
WRP 2
WRP k-1
WRP 3
WRP 1
Depth range k
WRP k
Equation. 3
L
Point cloud
Make depth grid based on color
Calculate L
Place WRP in the center of depth ranges (created based on L) and record all object points information on respective WRP. Then, CGH is created based on Fresnel diffraction.
Repeat for all colors (R,G, B)
Find L (LR, LG,LB) that created CGH in minimum time
Repeat for different active area dimension
Generate full color CGH based on LR, LG,LB
L
L
L
L
Notes: 1. Tomoyoshi Shimobaba, Nobuyuki Masuda, and Tomoyoshi Ito, "Simple and fast calculation algorithm for computer-generated hologram with wavefront recording plane," Opt. Lett. 34, 3133-3135 (2009)

## Slide 6: Change of no. of WRPs and object position effect calculation of CGH
Chart: Conventional M-WRP
| 2 | 4 | 8 | 16 | 32 | 64
 | 144.71 | 140.104 | 132.072 | 134.69 | 138.145 | 145.96
Chart: Calculation time using 8 WRPs
| 0 | 5 | 10 | 15
 | 132.072 | 132.764 | 133.397 | 134.863
a)
Notes: 1. Tomoyoshi Shimobaba, Nobuyuki Masuda, and Tomoyoshi Ito, "Simple and fast calculation algorithm for computer-generated hologram with wavefront recording plane," Opt. Lett. 34, 3133-3135 (2009)

## Slide 7: Change of no. of WRPs and object position effect calculation of CGH
Notes: 1. Tomoyoshi Shimobaba, Nobuyuki Masuda, and Tomoyoshi Ito, "Simple and fast calculation algorithm for computer-generated hologram with wavefront recording plane," Opt. Lett. 34, 3133-3135 (2009)

## Slide 8: Result
Three objects |  | Calculation time(sec.)
Conventional M-Method | 2 WRPs ∕ color × 3 | 243.406
 | 4 WRPs ∕ color × 3 | 242.114
 | 8 WRPs ∕ color × 3 | 241.613
 | 16 WRPs ∕ color x 3 | 248.276
 | 32 WRPs ∕ color ×3 | 254.84
 | 64 WRPs ∕ color × 3 | 269.456
MLDR method | 5 WRPs (Red) 5 WRPS(Green) 3 WRPS (blue) | 164.586
Fig. 5 : Reconstructed image for ‘three object’ using a) conventional M-WRP b) MLDR method
a) Conventional M-WRP
b) MLDR method
Notes: 1. Tomoyoshi Shimobaba, Nobuyuki Masuda, and Tomoyoshi Ito, "Simple and fast calculation algorithm for computer-generated hologram with wavefront recording plane," Opt. Lett. 34, 3133-3135 (2009)

## Slide 9
Conventional MWRP
Proposed method
Three items (1980 X1024) |  | Calculation time(sec.)
Conventional M-WRP Method | 2 WRPs ∕ color × 3 | 384.504
 | 4 WRPs ∕ color × 3 | 341.539
 | 8 WRPs ∕ color × 3 | 346.953
 | 16 WRPs ∕ color × 3 | 370.899
 | 32 WRPs ∕ color × 3 | 396.148
 | 48 WRPs ∕ color × 3 | 418.932
Proposed method | 2 WRPs (red) 2 WRPS(green) 4 WRPS (blue) | 298.737
Fig 2 : Depth ranges in conventional M-WRP
b)
a)
Result
Fig. 5 : Reconstructed image for ‘three object’ using a) conventional M-WRP b) MLDR method

## Slide 10
Conventional MWRP
Proposed method
Three items (1980 X1024) |  | Calculation time(sec.)
Conventional M-WRP Method | 2 WRPs ∕ color × 3 | 384.504
 | 4 WRPs ∕ color × 3 | 341.539
 | 8 WRPs ∕ color × 3 | 346.953
 | 16 WRPs ∕ color × 3 | 370.899
 | 32 WRPs ∕ color × 3 | 396.148
 | 48 WRPs ∕ color × 3 | 418.932
Proposed method | 2 WRPs (red) 2 WRPS(green) 4 WRPS (blue) | 298.737
Fig 2 : Depth ranges in conventional M-WRP
Result
Fig. 5 : Reconstructed image for ‘three object’ using a) conventional M-WRP b) MLDR method
a)
b)
c)

## Slide 11
Table 1 : Calculation time and PSNR comparison between conventional M-WRP and DM-WRP
Object | No. of object point | Resolution | No. of depth layer | Conventional M-WRP |  |  | Proposed DM-WRP |  | 
 |  |  |  | No. of WRP | Time(sec.) | PSNR(dB) | No. of WRP | Time(sec.) | PSNR(dB)
Three obj 1 | 84,549 | 190X1024 | 96 | 12 | 341.539 | 17.17 | 9 | 298.737 | 18.11
Three obj 2 | 35,263 | 190X1024 | 128 | 24 | 238.093 | 19.96 | 13 | 164.586 | 20.09
Papilion | 262,098 | 720X720 | 255 | 48 | 144.432 | 17.72 | 45 | 123.437 | 17.72
Results

## Slide 12
WRP 1
d
d
d
d
d
d
d
d
d
d
d
d
d
d
a)
b)
Depth
range 1
Depth
range 2
Depth
range 3
Depth
range 4
Depth
range 5
Depth
range 6
Depth
range 7
CGH
CGH
Depth
range n
N(z1) = 2
Depth
Range 2
WRP 1
N(z6) = 1
N(z7) = 1
N(z2) = 1
Depth
Range 1
WRP 2
N(z3) = 3
N(z4) = 3
N(z6) = 1
N(z7) = 2

## Slide 13
Active
area < k
Color < 3
Point cloud
Make depth grid based on color
Calculate L
Place WRP in the center of depth ranges (created based on L) and record all object points information on respective WRP. Then, CGH is created based on Fresnel diffraction.
Repeat for all colors (R,G, B)
Find L (LR, LG,LB) that created CGH in minimum time
Repeat for different active area dimension
Generate full color CGH based on LR, LG,LB
Acquisition of real objects using depth camera

## Slide 14
Point cloud
Make depth grid based on color
Calculate L
Place WRP in the center of depth ranges (created based on L) and record all object points information on respective WRP. Then, CGH is created based on Fresnel diffraction.
Repeat for all colors (R,G, B)
Find L that created CGH in minimum time (LR, LG,LB)
Repeat for different active area dimension
Generate full color CGH based on LR, LG,LB
Point cloud
Make depth grid based on color
Calculate L
Place WRP in the center of depth ranges (created based on L) and record all object points information on respective WRP. Then, CGH is created based on Fresnel diffraction.
Repeat for all colors (R,G, B)
Repeat for different active area dimension
Generate full color CGH based on LR, LG,LB
Find LR, LG, LB
Yes
No

## Slide 15
Point cloud
Make depth grid based on color
Calculate L
Place WRP in the center of depth ranges (created based on L) and record all object points information on respective WRP. Then, CGH is created based on Fresnel diffraction.
Repeat for all colors (R,G, B)
Find L that created CGH in minimum time (LR, LG,LB)
Repeat for different active area dimension
Generate full color CGH based on LR, LG,LB
Point cloud
Make depth grid based on color
Calculate L
Place WRP in the center of depth ranges (created based on L) and record all object points information on respective WRP. Then, CGH is created based on Fresnel diffraction.
Repeat for all colors (R,G, B)
Repeat for different active area dimension
Generate full color CGH based on LR, LG,LB
Find LR, LG, LB
Yes
No

## Slide 16
Chart: Max. length of depth reaage (cm)
| 0.61 | 0.65 | 0.69 | 0.73 | 0.77 | 0.81 | 0.85 | 0.89
 | 102.218 | 101.963 | 101.846 | 101.283 | 101.662 | 102.422 | 100.19 | 100.8
a)
b)
Point cloud
Make depth grid based on color
Calculate L
Place WRP in the center of depth ranges (created based on L) and record all object points information on respective WRP. Then, CGH is created based on Fresnel diffraction.
Repeat for all colors (R,G, B)
Repeat for different active area dimension C1, C2…..Ci
Generate full color CGH based on LR, LG,LB
Find LR, LG, LB
Yes
No

## Slide 17
Chart: Max. length of depth renage (cm)
| 0.61 | 0.65 | 0.69 | 0.73 | 0.77 | 0.81 | 0.85 | 0.89
 | 102.218 | 101.963 | 101.846 | 101.283 | 101.662 | 102.422 | 100.19 | 100.8
a)
b)